## Slide 1: Understanding the Impact of Route Reflection in Internal BGP
Ph.D. Final Defense
presented by Jong Han (Jonathan) Park
July 15th, 2011

## Slide 2: Research Overview
Internal Border Gateway Protocol and Route Reflection
Understanding the Impact of BGP Route Reflection
- Understanding BGP Next-hop Diversity (2nd author, Global Internet Symposium 2011)
- A Comparative Study of Architectural Impact on Next-hop Diversity (under submission to IMC’11)
- Quantifying i-BGP Convergence inside large ISPs (under submission to IMC’11)
BGP Route Reflection Protocol Diagnosis
- Investigating Occurrence of Duplicate Updates in BGP Announcements (PAM’10, Best Paper)
Others (listed as 2nd author) on BGP Performance
- Route Flap Damping with Assured Reachability (AINTEC’10)
- Explaining Slow BGP Table Transfers: Implementing a TCP Delay Analyzer (under submission to IMC’11)

## Slide 3: Motivation
Route reflection was added to the routing architecture to fix a few critical problems
Despite the wide adoption of RR, a systematic evaluation and analysis on the impact of route reflection is missing, which can be helpful in:
  Understanding of the protocol performance and enhancements
  More realistic simulations
  Designing the future routing protocols
This work is to fill in the void

## Slide 4: Outline
Introduction to Internal BGP and Route Reflection
Understanding BGP Path Diversity and the Impact of Route Reflection
Understanding BGP Convergence inside Large ISPs

## Slide 5: Introduction to full-mesh i-BGP
Total number of sessions = N(N-1)/2
Number of additional sessions for an additional i-BGP router = N
Total number of i-BGP routers in AS1 = 4 = N
AS1
AS2
AS3
AS4
e-BGP
i-BGP
This router is no longer needed. Remove!

## Slide 6: Full-mesh i-BGP does not scale
City 1
City 2
City 3
Large ISPs have hundreds or even more than a thousand routers internally
Full mesh leads to a high cost in provisioning
  Adding or removing a router requires reconfigurations of all other routers

## Slide 7: Addressing the scalability problem of full-mesh i-BGP
Two solutions are suggested in 1996
  AS confederations (RFC 1965)
  Route reflection (RFC 1966)
This work focuses on route reflection
  Dominant solution
  Main concerns shared with AS confederation
    Path diversity reduction
    Convergence delay

## Slide 8: Route reflection solves scalability problem
Total number of sessions = 4
Number of additional sessions for an additional i-BGP router = 1
Total number of i-BGP routers = 5 = N
AS1
AS2
route reflector
client 1
client 2
client 3
client 4
e-BGP
i-BGP

## Slide 9: Large ISP revisited with hierarchical RR
Route reflection substantially reduces the total number of sessions
Route reflection can be deployed hierarchically to reduce even more

## Slide 10: Negative Impact of BGP route reflection
Negative side effects
  Routing performance
    Path diversity [Uhlig, Networking’06]
    Convergence
    Others
      Robustness to failures
      Internal update explosion [McPherson,APNIC talk, 2009]
      Optimal route selection [Vutukuru, Infocom’06]
  Routing correctness
    Data forwarding loop [Griffin, Sigcomm’02]
    Route oscillations [McPherson, Internet Draft, 2000]

## Slide 11: Outline
Introduction to Internal BGP and Route Reflection
Understanding BGP Path Diversity and the Impact of Route Reflection
Understanding BGP Convergence inside Large ISPs

## Slide 12: Definitions
Next-hop POP and AS
  Next-hop Point-of-Presence (i.e., city in which the next-hop router is located) and AS that the ISP uses to reach a given external destination
BGP Next-hop Diversity
  Number of distinct next-hops to reach a given external destination as used simultaneously inside a given ISP

## Slide 13: Why do we care about path diversity?
Higher path diversity
  More flexibility in traffic engineering and load balancing
  Higher availability
Current IETF efforts to increase BGP diversity
  Diverse-path, Add-path, and External-best

## Slide 14: Path diversity reduction due to route reflection
AS1
RR
RTR2
RTR3
AS2, p
p: NH = RTR1, ASPATH = AS2
p: NH = RTR4, ASPATH = AS2
p: NH = RTR4, ASPATH = AS2
OTHERS
p: NH = RTR1, ASPATH = AS2
p: NH = RTR4, ASPATH = AS2
RTR1, RR
RTR1
RTR4
ALL

## Slide 15: Main questions to answer
What degree of BGP next-hop diversity do existing ISPs have now?
Does route reflection deployment reduce BGP next-hop diversity?

## Slide 16: Data collection settings
ISPFM: Tier-1 ISP with full-mesh i-BGP backbone routing infrastructure
ISPRR: Tier-1 ISP with route reflection i-BGP backbone routing infrastructure
i-BGP full-mesh
ISPFM
backbone sub-AS
Sub
AS
AS1
Sub
AS
Sub
AS
ASi
ISPRR
ASii
AS11
AS22
AS2
Collector
Collector
BGP router
Node type:
confederation BGP
1st level reflector
2nd level reflector
3rd level reflector
Session type:
i-BGP reflector to client
i-BGP peer
e-BGP peer

## Slide 17: BGP next-hop diversity of the 2 ISPs
ISPFM
ISPRR
Common observations
  A small number of prefixes with a very high degree of next-hop diversity
  Prefixes with very low degree (diversity=1) of next-hop diversity
  A few large groups of prefixes with the same moderate degree of next-hop diversity
  A significant number of prefixes (more than 90% and 65% respectively) have multiple next-hop POPs and ASes
Overall, ISPRR has relatively lower next-hop diversity, compared to ISPFM

## Slide 18: Inferring external connectivity
AS1
R2
R1
AS2, p
R3
R4
AS3
In the absence of failures, the reachability through R2 is not visible
If the current best path fails, the path through R2 will be explored

## Slide 19: Inferred external connectivity vs. next-hop POPs
The external connectivity is not the main reason for the difference
ISPFM (during 1st week of June 2010)
ISPRR (during 1st week of June 2010)

## Slide 20: Paths can be hidden due to path preference
7 BGP path attribute values used by a BGP router in BGP best path selection
  First 4 are independent from the i-BGP topological location of the given router
    LOCAL_PREF
    AS_PATH length
    ORIGIN
    MED
  The rest 3 attribute values change depending on the i-BGP topological location of the given router
    Prefer e-BGP over i-BGP
    IGP cost
    Router ID

## Slide 21: Diversity reduction by the first 4 BGP path attributes
The first 2 criteria of BGP path selection hides the majority of the path diversity
  About 16% and 10% reduction for ISPFM and 34% and 7.6% reduction for ISPRR by (1) LOCAL_PREF and (2) AS_PATH length respectively
ISPFM (during 1st week of June 2010)
ISPRR (during 1st week of June 2010)

## Slide 22: Summary
The overall next-hop diversity varies widely, depending on the topological location of origin AS for a given prefix
The difference in the overall next-hop diversity is due to i-BGP topology-independent factors
  More specifically, the first 2 BGP best selection criteria hides up to 42%
Next-hop diversity reduction by ISPRR’s hierarchical RR is less than 3.3%
  Main reason. significant reduction by the i-BGP topology-independent factors already

## Slide 23: Outline
Introduction to internal BGP and Route Reflection
Understanding BGP Path Diversity and the Impact of Route Reflection
Understanding BGP Convergence inside Large ISPs

## Slide 24: Definitions
Event
  Change in routing information to reach a given external prefix
Monitor
  Router from which i-BGP data is collected within a given ISP
i-BGP convergence
  Convergence of all monitors inside a given ISP for a given event

## Slide 25: Why do we care about i-BGP convergence?
BGP suffers from slow convergence
  May cause severe performance problems in data delivery [TON’01, Labovitz] [Infocom’01,Labovitz] [IMC’03,Mao] [Sigcomm’06,Wang] at inter-AS level
  Virtually no measurement studies exist on BGP convergence inside an ISP

## Slide 26: Increased convergence delay in i-BGP RR
AS1
RTR 1
RR1
RTR 2
RR2
AS2, p
Update path
RR2->RTR1
RR1->RTR1
RR2->RR1->RTR1
RR1->RR2->RTR1
Not reachable
There is no path to prefix p!
1. Delay due to hierarchy
- additional path distance
- additional processing delays
2. Delay due to route reflector redundancy
- increased # of control paths
RTR 3
RTR 4

## Slide 27: Main questions to answer
What does i-BGP convergence look like?
What is the impact of route reflection convergence delay?

## Slide 28: Data collection settings
ISPFM: the collector is a member of the i-BGP full-mesh
ISPRR: the collector is a client of the 2nd level route reflectors
i-BGP full-mesh
ISPFM
backbone sub-AS
Sub
AS
AS1
Sub
AS
Sub
AS
ASi
ISPRR
ASii
AS11
AS22
AS2
Collector
Collector
BGP router
Node type:
confederation BGP
1st level reflector
2nd level reflector
3rd level reflector
Session type:
i-BGP reflector to client
i-BGP peer
e-BGP peer

## Slide 29: Inferring best path selection for peers in i-BGP full-mesh
Q: Best path used by RTR3 to reach prefix p?
A: Use geographical information of the routers to approximate IGP cost
in the BGP best path selection
AS1
RTR1
Path1 to prefix p
RTR2
RTR3
Path2 to prefix p
Which path does RTR3 use?
Collector
SelectBestPath(Path1,Path2)
LOCAL_PREF
AS_PATH length
ORIGIN
MED
E-BGP over I-BGP
IGP cost to the path
Router ID (tie breaker)

## Slide 30: High-level view of quantifying i-BGP convergence
monitorn
monitor1
collector
Event Identification
(update clustering)
event e
event e
T = 60 seconds
path preference
T
S
METRICS
1. Duration(e)
2. NumUpdates(e)
3. NumPaths(e)
Event Classification
(Determine Type & Scale)

## Slide 31: Event identification: time-based update clustering
X = 60 seconds
ISPFM
Inter-arrival times of beacon prefix updates during June 2010 (seconds)
Fraction of updates (CCDF)
Time
Example of update arrivals for a given beacon prefix
7200 seconds
7200 seconds

## Slide 32: Event classification: adding type information
EventM
Path Disturbance
Path Change
Same Path
Idist
Ispath
Iequal
Ishort
Ilong
Iup
Idown
Time
p0
p1
pn
p0 = pn
p0 != pn
p0 = … = pn
Updates generated from a monitor in an event
[IMC’06 Oliveira]
The last update from the previous event
ISPFM 8.9% 3.0% 3.1% 35.8% 40.1% 0.3% 8.8%
ISPRR 15.7% 4.9% 4.6% 29.7% 31.9% 0% 13.2%

## Slide 33: Event classification: adding scale information
Event Scale
  Se = (# of POPs observed the event) / (total # of monitored POPs)
Event Scale Types
  Local Event: only one POP inside the ISP observes the event
  AS-wide Event: all POPs inside the ISP observe the event
  Others: non-local or non-AS-wide events

## Slide 34: Identified events from ISPRR and ISPFM
The total number of events gradually increases as it fluctuates
Most of events are either local or AS-wide in their scale
Local events are observed in all POPs
Number of Identified Events per Month
Scale of Events During June 2010

## Slide 35: Event characteristics
The majority of local events converge within 1 second
  97% and 72% for ISPRR and ISPFM respectively
  Difference due to the different delays of the neighboring ASes
AS-wide event duration differs between the two ISPs
  Due to the delayed updates via different paths
ISPFM
ISPRR
Local Events
AS-wide Events

## Slide 36: How Much Delay Does Route Reflection Add to the Overall i-BGP Convergence?

## Slide 37: Case studies in ISPRR: estimating the additional delay caused by route reflection
Additional delays due to route reflector redundancy
  Identify the superfluous updates generated purely due to route reflector redundancy
  What is the additional convergence time solely contributed by these updates?
Additional delays due to hierarchy
  Compare the direct and RR paths between all monitors in the backbone routing infrastructure inside ISPRR

## Slide 38: Superfluous update example
ISPRR
BR1
BR2
How many superfluous updates?
What is the additional delay caused by these updates?

## Slide 39: Superfluous updates due to route reflector redundancy and its Impact on convergence
The amount of superfluous updates is not significant in most cases
  Convergence duration: 0.3%, 0.2%, 0.4% and 5.3% for Iup, Ishort, Ilong and Idown increase
  Number of updates: 3%, 4%, 13%, and 40% increase for Iup, Ishort, Ilong, and Idown increase

## Slide 40: Is there routing plane path stretch in the top 2-levels of route reflection inside ISPRR?
Measure the physical path length and latency for RR paths using traceroute and ping
Repeat the measurement for direct paths and compare with RR paths
DistanceDirect(AA,BB) =
A
B
AA
BB
where ri is a router in the order detected by traceroute
DistanceRR(AA,BB) =
DistanceDirect(AA,B) + DistanceDirect(B,BB)

## Slide 41: Path distance and latency of direct and RR paths
In case of ISPRR, RR paths are shorter with less latency
  i.e., the RRs are aligned well with the shortest physical paths

## Slide 42: Summary
Defined, quantified, and analyzed i-BGP convergence
i-BGP routing events mostly are local or AS-wide in their scale
  Local events: mostly lasts less than 1 second
  AS-wide events: the duration is longer and mostly depends on external factors
  Our case study of ISPRR shows
    RR does increase the number of updates and convergence duration
    However, the amount is not significant
      Additional 0.3%, 0.2%, 0.4%, and 5.3% increase in the duration of Iup, Ishort, Ilong, and Idown
    RR topology design can mitigate the additional delays

## Slide 43: Thank you.

## Slide 44: Backup Slides

## Slide 45: Paths can be hidden due to path preference
In BGP, a less preferred path is not announced by the border routers
In this example, external connectivity: 3 POPs, next-hop diversity: 2 POPs
AS1
R2
R1
AS2, p
R3
R4
AS3

## Slide 46: Topology-independent diversity reduction in ISPFM
LOCAL_PREF and AS_PATH length are the two main impacting attributes that hide paths
  About 16% and 10% respectively

## Slide 47: Topology-independent diversity reduction in ISPRR
Significant reduction mostly due to the LOCAL_PREF value
  About 34% and 7.6% by LOCAL_PREF and AS_PATH length respectively

## Slide 48: Event characteristics
The majority of local events converge within 1 second
  97% and 72% for ISPRR and ISPFM respectively
i-BGP convergence duration differs between the two ISPs
  Due to the difference in connectivity and delayed updates via different paths
ISPFM
ISPRR
Local Events
AS-wide Events

## Slide 49: Update reduction in full-mesh i-BGP
Setting
  Data: NTT i-BGP data from 20100601
  Apply different MRAI timers to the monitor-collector session and calculate the reduction for beacon prefixes
Observation
  Higher MRAI timer leads to update reduction, and the update reduction is not significant

## Slide 50: Increased convergence time in full-mesh i-BGP
Setting
  Data: NTT i-BGP data from 20100601
  Apply different MRAI timers to the monitor-collector session and calculate the convergence duration for beacon prefixes
Observation
  The increased convergence time is proportional to the MRAI timer used

## Slide 51: Update reduction in i-BGP HRR
Setting
  Data: Level3 i-BGP data from 20100603
  Apply different MRAI timers to the monitor-collector session and calculate the reduction for beacon prefixes
Observation
  Reduction MRAI timer with 1 second effective enough; the update propagation and the internal path exploration for a given external path is mostly under 1 second within the ISP

## Slide 52: Increased convergence time in i-BGP HRR
Setting
  Data: Level3 i-BGP data from 20100603
  Apply different MRAI timers to the monitor-collector session and calculate the convergence duration for beacon prefixes
Observation
  The increased convergence time is proportional to the MRAI timer used in Iup